## Slide 1: Project Apollo
Why
  Ventilators need oxygen! (typical FiO2 0.3 … 0.5)
  Oxygen generation is a big problem in developing countries
  People are already looking at alternative (local) ways for producing oxygen
Apollo Control Box v4
  Universal control box
    Should work with any PSA-based O2 concentrator
  Focus
    Safety: detect all failure scenarios
    Ease of use: User experience and maintainability. Clear, actionable error messages
  What is it = Self-contained control box
    Large (3.5”) touch screen for diagnostic messages, medical-grade buzzer
    Open source, modular PCB design. Works with a variety of sensors
    New: self-tuning (valve timing, auto-adjusts to changes in compressed air input pressure, machine learning)
  Patient sensor/data integration (optional)
    SpO2 oximeter Bluetooth sensors, detecting breathing pattern to optimize O2 flow
    Continuous and pulse mode of operation. Pulse mode = key to greatly reduces compressor size and power consumption
  Status
    v1..v3 designs published and tested, with Apollo O2 concentrator reference design
    Working on v4 (ETA November 2020 for first prototypes)
Collaborations
  Helpful Engineering, Public Invention, Oxikit, Microsoft Garage, Quick2space.org
Documentation, code
  http://project-apollo.org