## Slide 1: Apollo Control Box
  Goal = Self-contained control box
    Focus
      Safety: detect all failure scenarios
      Ease of use: User experience and maintainability. Large (3.5”) touch screen for diagnostic messages, medical-grade buzzer
    Can drive with PSA-based O2 concentrator (Oxikit, PIOC, Apollo reference O2 concentrator)
      Open source, modular PCB design. Works with a variety of sensors
    Self-tuning AI
      learning mode for adjusting valve timing, auto-adjusts to changes in compressed air input pressure
    Continuous and pulse mode of operation
      Adjust PSA operational cycle in sync with patient breathing
      Pulse mode = key to greatly reduces compressor size and power consumption
  Patient sensor/data integration
    O2 flow regulation: adjust O2 flow in response to oximeter readings
      SpO2 oximeter Bluetooth sensors
      Breathing rate detection through pressure sensors and flow rate measurement
    GTS/Teladoc integration
      push medical data to the cloud for doctors to remotely monitor patients)
  Integration
    Oxikit: proportional valve flow control, GTS/Teladoc integration, Bluetooth oximeter
    PIOC, Oxikit: control box
    LifeMech – ventilator integration (TBD)
  Status
    v1..v3 designs published and tested, with Apollo O2 concentrator reference design
    Apollo control box: Working on v4 (ETA November/December 2020 for first prototypes)
    Pursuing GTS/Teladoc prototyping with Oxikit

## Slide 2: PSA/Ventilator integration points
Goal
  Unified solution?
Requirements
  Breathing rate detection
    Ventilator can provide that info
    Enables efficient pulse mode operation at PSA concentrator level
  Flow regulation
    Adjusts O2 concentration dynamically by adjusting PSA timings
    Oximeter pulse reading (Bluetooth)
  GTS/Teladoc integration
    Patient data (SpO2 data)

## Slide 3: Prototypes